## Slide 1: Compute Express Link™ (CXL): Exploring Coherent Memory and Innovative Use Cases
March 12, 2020

## Slide 2: Compute Express Link™ (CXL) Overview
Processor Interconnect:
  Open industry standard
  High-bandwidth, low-latency
  Leverages PCI Express®
  Coherent interface
  Targets high-performance computational workloads
    Artificial Intelligence
    Machine Learning
    HPC
    Comms
A new class of interconnect for device connectivity
2
Compute Express Link™ and CXL Consortium™ are trademarks of the Compute Express Link Consortium.
December CXL Consortium Webinar:
Introduction to Compute Express Link (CXL)
https://www.youtube.com/watch?v=RpAshNmpqLQ
Today’s Focus

## Slide 3: Today’s Presenters
Rob Blankenship
    CXL Consortium™ Memory Working Group Member
    Processor Architect and Principal Engineer, Intel
Kurt Lender CXL Consortium™ Marketing Working Group Co-Chair
Senior Ecosystem Enabling Manager, Data Center Group, Intel
    Siamak Tavallaei
    CXL Consortium™ Technical Task Force Co-Chair
    Principal Architect, Microsoft Azure
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 4: Compute Express Link™ (CXL): Coherency Use Cases
Copyright © 2020 CXL Consortium™ | All Rights Reserved
Siamak Tavallaei
CXL Consortium™ Technical Task Force Co-Chair
Principal Architect, Microsoft Azure

## Slide 5: CXL Enables New Use-cases
Memory Expansion beyond CPU-attached Memory
Accelerators & NICs sharing memory with the Host CPU
Modular systems
Disaggregated computing
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 6: Emerging Architectures Based on Different Network Topologies
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 7: Two-layered View: Fabric Components vs. Compute
Homogeneous vs. Heterogeneous
Homogeneous: Peer-to-peer
Heterogeneous: Host interface to Device
  Host-to-accelerator
  Host-to-storage
  Host-to-memory
Natively Scale-up vs. Networked Scaled-out
Native Expansion (CPUs, Accelerators, etc.)
Expansion via the Network (Ethernet, InfiniBand, etc.)
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 8: Competing Interconnects have Emerged
Interconnects
  CPU-centric
  Accelerator-centric
  Memory-centric
Data Movement
  Coherent and Load/Store optimized for control plane
  Block-mode DMA/RDMA optimized for IO and data-plane throughput
Local Interconnect vs. Rack/Datacenter scope
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 9
The industry is converging on the non-CPU interconnect….
Focus on:
Compute Express Link
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 10: Opportunities Enabled by CXL
As an efficient interconnect, CXL opens several opportunities:
Accelerator Interface
  AI & HPC
  Computational Storage for Databases, etc.
  Network Accelerators
Memory Interface (for DRAM and storage-class memory, Load/Store memory)
Bridges and Gateways for compute access to components on a larger Fabric
  Broader Fabrics for memory,
  Compute disaggregation, and
  Storage-class memory
New CXL/Memory Form Factor
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 11
Compute Express Link™
CXL 1.1
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 12: What is CXL?
CXL runs across the standard PCIe physical layer with new protocols optimized for cache and memory
CXL uses a flexible processor Port that can auto-negotiate to either the standard PCIe transaction protocol or the alternate CXL transaction protocols
First generation CXL aligns to 32 GT/s PCIe 5.0 specification
CXL usages expected to be key driver for an aggressive timeline to PCIe 6.0 architecture
x16 PCIe
Card
X16 Connector
x16 CXL
Card
  Processor
PCIe channel
SERDES
Connector
etc.
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 13: CXL Protocols
The CXL transaction layer comprises three dynamically multiplexed protocols on a single Link:
CXL.io – Discovery, configuration, register access, interrupts, RAS, etc. (similar to PCIe)
CXL.cache – Device access to processor-attached memory more efficiently
CXL.memory – Processor access to device-attached memory
CXL Link dynamically multiplexes IO, Cache, and Memory Protocols
in Flit Format on PCIe PHY Layer
Accelerator
Accelerator Logic
CXL.io
Discovery
Register Access
Configuration
Initialization
Interrupts
DMA
ATS
CXL.cache
Memory Flows
Coherent Requests
Optional
Device Memory
CXL.memory
Memory Flows
Host Processor
Coherence and Memory Logic
PCIe/CXL.io
Logic
Host Memory
CXL.cache
CXL.memory
CPU Core
CPU Core
Internal
IO Devices
CXL.io
Converged Memory
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 14: Heterogeneous Computing, Revisited
CXL enables a more fluid and flexible memory model:
Single, common, memory address space across processors and devices to enhance PCIe architecture for heterogeneous computing and server disaggregation
Low-latency, Load/Store access to memory: Host to Device and Device to Host
User-level & Kernel-level data access and data movement
More efficient population and update of operands
More efficient extraction of results
Memory resource “borrowing”
Memory Load/Store
GPU
FPGA
AI
CPU
CPU
NIC
NIC
CPU-attached Memory
(OS Managed)
Accelerator-Attached Memory
(Runtime managed cache)
…
…
“Writeback”
Memory
Memory
Load/Store
PCIe DMA
PCIe DMA
“Writeback”
Memory
…
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 15: The Way It Is with PCIe Now:
Copyright © 2020 CXL Consortium™ | All Rights Reserved
Non-cacheable memory access
Optimized for Throughput via Block Moves
Isolated memory pools
Block-accessed memory semantics via PCIe DMA
Descriptors, Doorbells, & Interrupts
Resource sharing via Block Moves
Moving operands and results back and forth between accelerators
Memory Load/Store
GPU
FPGA
AI
CPU
CPU
NIC
NIC
CPU-attached Memory
(OS Managed)
Accelerator-Attached Memory
(Runtime managed cache)
…
…
“Writeback”
Memory
PCIe DMA
PCIe P2P
PCIe DMA
“UnCached”
Memory
…

## Slide 16: Representative CXL Usages
Simplify programing model & enhance performance
Type 1: Caching Devices & Accelerators
Usages:
  PGAS NIC (shared address space)
  NIC atomics
Protocols:
  CXL.io
  CXL.cache
CXL
Accelerator
NIC
Cache
DDR
DDR
Processor
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 17: Representative CXL Usages
Simplify programing model & enhance performance
Type 3: Memory Buffers
Usages:
  Memory BW expansion
  Memory capacity expansion
  2LM
Protocols:
  CXL.io
  CXL.memory
Memory
Memory
Memory
Memory
CXL
DDR
DDR
Processor
Memory
Buffer
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 18: Representative CXL Usages
Simplify programing model & enhance performance
Type 2: Accelerators with Memory
Usages:
  GPU
  Dense Computation
Protocols:
  CXL.io
  CXL.cache
  CXL.memory
CXL
DDR
DDR
Processor
HBM
HBM
Accelerator
Cache
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 19: Summary: Representative CXL Usages
Simplify programing model & enhance performance
Type 1: Caching Devices & Accelerators
Usages:
  PGAS NIC (shared address space)
  NIC atomics
Protocols:
  CXL.io
  CXL.cache
Type 2: Accelerators with Memory
Usages:
  GPU
  Dense Computation
Protocols:
  CXL.io
  CXL.cache
  CXL.memory
Type 3: Memory Buffers
Usages:
  Memory BW expansion
  Memory capacity expansion
  2LM
Protocols:
  CXL.io
  CXL.memory
CXL
Accelerator
NIC
Cache
DDR
DDR
Processor
CXL
DDR
DDR
Processor
HBM
HBM
Accelerator
Cache
Memory
Memory
Memory
Memory
CXL
DDR
DDR
Processor
Memory
Buffer
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 20: CXL Coherency Intro
Copyright © 2020 CXL Consortium™ | All Rights Reserved
Rob Blankenship
CXL Consortium™ Memory Working Group Member
Processor Architect and Principal Engineer, Intel

## Slide 21: Goals / Topics
CXL protocols
Cache coherence introduction
How CXL fits in a CPU cache hierarchy
CXL coherence protocol introduction
Flow examples
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 22: CXL Uses 3 Protocols
IO (CXL.io) → Same as PCI Express®
Memory (CXL.mem) → Memory Access from CPU Host to Device
Cache (CXL.cache) → Coherent Access from Device to CPU Host
Copyright © 2020 CXL Consortium™ | All Rights Reserved
F0
Fn
F1
….
CPU Host
IO Bridge
IOMMU
Coh Bridge
CXL Device
Coherent Cache
Cache
Home Agent
Memory Controller
Memory
Host Memory
Device Memory
Memory
Controller
IO
DMA Engine
MMIO/CFG Target
Cache
Memory
IO

## Slide 23: Caching Overview
Caching temporarily brings data closer to the consumer
Improves latency and bandwidth using prefetching and/or locality
Definitions for cache use:
  Prefetching: Loading Data into cache before it is required
  Spatial Locality (locality is space): Access address X then X+n
  Temporal Locality (locality in Time): Multiple access to the same Data
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 24: Example CPU Cache Hierarchy with CXL
Modern CPUs have 2 or more levels of coherent cache
Lower levels (L1), smaller in capacity with lowest latency and highest bandwidth per source.
Higher levels (L3), less bandwidth per source but much higher capacity and support more sources
Note: Cache/Memory capacities are examples and not aligned to a specific product.
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 25: Cache Consistency
How do we make sure updates in cache are visible to other agents?
Invalidate all peer caches prior to update
Can managed with software or hardware  CXL uses hardware coherence
Define a point of “Global Observation” (aka GO) when new data is visible from writes
Tracking granularity is a “cacheline” of data  64-bytes for CXL
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 26: Cache Coherence Protocol
Modern CPU caches are built on M,E,S,I protocol/states
  Modified – Only in one cache, Can be read or written, Data NOT up-to-date in memory
  Exclusive – Only in one cache, Can be read or written, Data IS up-to-date in memory
  Shared – Can be in many caches, Can only be read, Data IS up-to-date in memory
  Invalid – Not in cache
M,E,S,I is tracked for each cacheline address in each cache
  Cacheline address in CXL is Addr[51:6]
Notes:
  Each level of the CPU cache hierarchy follows MESI and layers above must be consistent
  Other extended states and flows are possible but not covered in context of CXL
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 27: How are Peer Caches Managed?
All peer caches managed by the “Home Agent” within the cache level
A “Snoop” is the term for the Home to check cache state and causing cache state changes
Example CXL Snoops:
  Snoop Invalidate (SnpInv): Cache to degrade to I-state, and must return any Modified data
  Snoop Data (SnpData): Cache to degrade to S-state, and must return any Modified data.
  Snoop Current (SnpCurr): Cache state does not change, but must return any Modified data
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 28: MESI Transitions in CXL
Device Request
Snoop Invalidate
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 29: Read Flow
Diagram to show message flows in time
  X-axis: Agents
  Y-axis: Time
Copyright © 2020 CXL Consortium™ | All Rights Reserved
Memory
Controller
CXL
Device
Peer
Cache
Home
I
E
Legend
Cache State:
  Modified
  Exclusive
  Shared
  Invalid
Allocate Tracker
Deallocate Tracker

## Slide 30: Read Flow
Diagram to show message flows in time
  X-axis: Agents
  Y-axis: Time
Copyright © 2020 CXL Consortium™ | All Rights Reserved
Memory
Controller
CXL
Device
Peer
Cache
Home
SnpData
RdShared
MemRd
DATA
I
E
I  S
RspSHitSE
Data
E  S
GO-S
Legend
Cache State:
  Modified
  Exclusive
  Shared
  Invalid
Allocate Tracker
Deallocate Tracker

## Slide 31: Mapping Flow Back to CPU Hierarchy
CXL
Device
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 32: Mapping Flow Back to CPU Hierarchy
Peer Cache can be:
  Peer CXL Device with Cache
  CPU Cache in Local Socket
  CPU Cache in Remote Socket
CXL
Device
Peer
Cache
Peer Cache
Peer Cache
Peer Cache
Peer Cache
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 33: Mapping Flow Back to CPU Hierarchy
Peer Cache can be:
  Peer CXL Device with Cache
  CPU Cache in Local Socket
  CPU Cache in Remote Socket
Memory Controller can be:
  Native DDR on Local Socket
  Native DDR on Remote Socket
  CXL.mem on peer Device
CXL
Device
Peer
Cache
Home
Peer Cache
Peer Cache
Home
Memory
Controller
Memory
Controller
Memory
Controller
Memory
Controller
Peer Cache
Peer Cache
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 34: Example #2: Write
For Cache Writes there are three phases:
  Ownership
  Silent Write
  Cache Eviction
Legend
Cache State:
  Modified
  Exclusive
  Shared
  Invalid
Allocate Tracker
Deallocate Tracker
CXL
Device
Peer
Cache
Home
I
S
Copyright © 2020 CXL Consortium™ | All Rights Reserved
Memory
Controller

## Slide 35: Example #2: Write
For Cache Writes there are three phases:
  Ownership
  Silent Write
  Cache Eviction
Legend
Cache State:
  Modified
  Exclusive
  Shared
  Invalid
Allocate Tracker
Deallocate Tracker
Ownership
CXL
Device
Peer
Cache
Home
I
S
SnpInv
RdOwn
MemRd
I  E
Data
S  I
GO-E
RspI HitSE
DATA
Copyright © 2020 CXL Consortium™ | All Rights Reserved
Memory
Controller

## Slide 36: Example #2: Write
For Cache Writes there are three phases:
  Ownership
  Silent Write
  Cache Eviction
Legend
Cache State:
  Modified
  Exclusive
  Shared
  Invalid
Allocate Tracker
Deallocate Tracker
Ownership
Write
CXL
Device
Peer
Cache
Home
I
S
SnpInv
RdOwn
MemRd
I  E
Data
S  I
GO-E
RspI HitSE
DATA
Copyright © 2020 CXL Consortium™ | All Rights Reserved
E  M
Memory
Controller
<Silent Wr>

## Slide 37: Example #2: Write
For Cache Writes there are three phases:
  Ownership
  Silent Write
  Cache Eviction
Legend
Cache State:
  Modified
  Exclusive
  Shared
  Invalid
Allocate Tracker
Deallocate Tracker
Ownership
Write
Eviction
CXL
Device
Peer
Cache
Home
I
S
SnpInv
RdOwn
MemRd
I  E
Data
S  I
GO-E
RspI HitSE
DATA
Copyright © 2020 CXL Consortium™ | All Rights Reserved
E  M
DirtyEvict
MemWr
Cmp
GO_WritePull
Data
M  I
Memory
Controller
<Silent Wr>

## Slide 38: Coherence Summary How does coherency help a CXL Device?
Break out of IO ordering model:
  Prefetching data before reading flag  saves latency
  Streaming WRITEs to memory get a completion  PGAS NIC use model
  WRITE data committed within local cache
Data Reuse (cache locality) reduces latency and bandwidth demand
  Descriptor or Semaphore Polling
Complex Atomics  Needed by accelerators and NICs
CXL.mem can expose Device memory as coherent  No DMA required
  Host or peer can pull current data from Device when it is ready to consume  reduce data copies
  Enables host/peer to prefetch data
Not Risk Free!
  Badly behaving Device or use model can impact system performance
  Conflicts to single cache-line may cause serializing events  Spinlock across many devices/threads
  Device should adopt best known practices for CPU coherence flow: TicketLock, LRU cache, etc.
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 39: About the CXL Consortium™
Copyright © 2020 CXL Consortium™ | All Rights Reserved
Kurt Lender
CXL Consortium Marketing Working Group Co-Chair
Senior Ecosystem Enabling Manager, Data Center Group, Intel

## Slide 40: CXL Consortium Overview
CXL Consortium boasts 90+ member companies to date and is growing rapidly
  Current membership ranks reflects the required industry expertise to create a robust, vibrant CXL ecosystem
CXL Consortium Work Groups:
  5 Technical (Protocol, PHY, Software & Systems, Memory, Compliance) and Marketing
CXL Board of Directors:
40
Copyright © 2020 CXL Consortium™ | All Rights Reserved
Notes: Two levels of membership are available for participation in CXL
  Adopter memberships are free and allow your company to:
    Access the final specification releases
    Gain IP protection as outlined in the IPR Policy and Membership Agreements
  Contributor membership are $20K for the first year and $10K per year each subsequent year with the following added benefits:
    Participate in the CXL workgroups
    Influence the direction of the technology
    Access the intermediate specifications (dot level releases)

## Slide 41: Join Today! www.computeexpresslink.org/join Follow Us on Social Media
41
@ComputeExLink
www.linkedin.com/company/cxl-consortium/
Copyright © 2020 CXL Consortium™ | All Rights Reserved
CXL Consortium Channel

## Slide 42: Thank You
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 43: Audience Q&A
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 44
Compute Express Link™
CXL 1.1 Backup
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 45: Emerging CXL (Compute Express Link)
An industry attempt to converge disparate interconnects for compute and memory
  Help focus supplier energy
  Help promote adoption
Backed by all major industry players:
  CPU vendors
  System vendors
  Hyperscalers
  Component Suppliers
CXL will be a major factor in Interconnect Standards!
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 46: CXL Stack – Designed for Low Latency
All 3 representative usages have latency-critical elements:
  CXL.cache
  CXL.memory
CXL cache and memory stack is optimized for latency:
  Separate transaction and link layer from IO
  Fixed message framing
CXL io flows pass through a stack that is largely identical to a standard PCIe stack:
  Dynamic framing
  Transaction Layer Packet (TLP)/ Data Link Layer Packet (DLLP) encapsulated in CXL flits
CXL Stack – low latency Cache and Mem Transactions
Alternate Stack – for contrast
PCIe
Transaction
Layer
CXL
Transaction
Layer
CXL.cache/CXL.mem
Transaction Layer
PCIe
Link
Layer
CXL
Link
Layer
CXL.cache/CXL.mem
Link Layer
PCIe/CXL Logical Phy
CXL Dynamic Mux
PCIe/CXL Analog Phy
Static Mux
PCIe
Transaction
Layer
Alternate Link
Transaction Layer
PCIe
Link
Layer
PCIe Logical Phy
Dynamic Mux
PCIe Analog Phy
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 47: CXL’s Protocol Asymmetry
The CXL coherency protocol is asymmetric
Several key advantages:
  Avoid protocol interoperability hurdles/roadblocks
  Enable devices across multiple segments (e.g. client and server)
  Enable Memory buffer with no coherency burden
  Simpler, processor independent device development
CCI Model – Symmetric CCI Protocol
CXL Model – Asymmetric Protocol
Accelerator
CPU
Accelerator Engine
Accelerator Caching Agent
Accelerator Home Agent
Memory Agent
CCI Caching Agent
CCI Home Agent
Memory Agent
CCI
Core
Core
Core
Core
Accelerator
CPU
Accelerator Engine
Memory Agent
Biased
Coherence
Bypass
CXL/CCI Caching Agent
CXL/CCI Home Agent
Memory Agent
Core
Core
Core
Core
CXL
CXL
Cache
CCI –Cache Coherent Interconnect
CCI –Cache Coherent Interconnect
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 48: CXL’s Coherence Bias
Critical access class for accelerators is
“device engine to device memory”
“Coherence Bias” allows a device engine to access its memory coherently without visiting the processor
Two driver managed modes or “Biases”
HOST BIAS: pages being used by the host or shared between host and device
DEVICE BIAS: pages being used exclusively by the device
Both biases guaranteed
Correct/coherent
Guarantee applies even when software bugs or speculative accesses unexpectedly access device memory in the “Device Bias” state.
Accelerator
CPU + IO
Coherence
CA + HA
Accelerator Local Memory
Host Memory
Uncached
Flow
Cache
Device Bias
Accelerator
Host Bias
Accelerator
CPU + IO
Host Memory
Coherence
CA + HA
Accelerator Local Memory
Accelerator
CPU
Accelerator Engine
Memory Agent
Biased
Coherence
Bypass
CXL/CCI Caching Agent
CXL/CCI Home Agent
Memory Agent
Core
Core
Core
Core
Cache
Cache
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 49: CXL Summary
CXL has the right features and architecture to enable a broad, open eco-system for heterogeneous computing and server disaggregation
PCIe foundation and asymmetric architecture for broad adoption and interoperability across segments and developers (on both ends of the wire)
Low latency for memory driven application models
Three mix-and-match protocols for a wide variety of usages
A cache coherency scheme, “Coherence Bias”, designed for the heterogeneous device-driven
computing paradigm-- not homogeneous multi-socket processor coherency
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 50
Compute Express Link™
CXL 2.0 Efforts
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 51: Technical WG Scopes
Technical WG | Primary Coverage in WG
Protocol | CXL.Cache, CXL.Mem, CXL.io, CXL.Cache/Mem Link Layer
Software & Systems | Application Software, Middleware, Device Driver and Multi-Domain/ Switch Management RAS, Reset, Platform, Enumeration and Discovery
PHY | PHY, Link Power, Arbitration and Protocol Muxing
Compliance | Compliance
Memory System | Input to TTF on the broader set of system-level, memory-related features for future consideration
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 52: Backup
Copyright © 2020 CXL Consortium™ | All Rights Reserved
52

## Slide 53: Conflict Resolution
Conflicts occur when multiple caches want access at the same time.
Most of the complexity in coherence protocol will be from handling these cases.
Required to give each cache opportunity to read and/or write a cacheline after GO and must ensure MESI rules.
Secondary goals:
  Minimizing overhead to non-conflicting cases (Majority of cases)
  Resolve conflicts quickly.
B
C
H
I
I
MC
RdShared
SnpInv
RdOwn
RspI
MR
DATA
I  E
GO-E
SnpData
I  S
GO-S
Data
Data
RspIHitI
DATA
MR
MESI Violation!
Copyright © 2020 CXL Consortium™ | All Rights Reserved

## Slide 54: CXL Conflict Resolution Rule(s)
CXL Ordering RULE: Snoops must PUSH GO for same address.
Snoop waits for Data after GO
Other protocols resolve this in different ways.
MC
B
C
H
I
I
RdShared
SnpInv
RdOwn
RspIHitS
MR
DATA
I  E
GO-E
SnpData
I  S
GO-S
Data
Data
RspIHitI
DATA
MR
Snoop PUSH GO
S  I
Copyright © 2020 CXL Consortium™ | All Rights Reserved